## Slide 1: A Mixed-Criticality MPSoC Case-Study
The Multi-Rotor Avionics and Payload Computer System
Sören Schreiner, M.Sc. – OFFIS e.V.

## Slide 2: Multi-rotor system demonstrator
~ 60cm Aluminium/Carbon Frame
~ 2.4kg
Rapidly rotating Propellers
~ 60km/h
!!! SAFETY-CRITICAL SYSTEM !!!
Notes: Motivation:
Kopter als fliegende Plattform, die allerdings trotz der kleinen größe sicherheitskritiisch ist
Können Nutzlast mitnehmen
Bisher onboard processing durch weitere hardware, die augf dem kopter mitgeführt wird
Mit CONTREX die einführung von mixed criticality
Payload Processing und flight algorithms auf einem single chip

## Slide 3: Multi-rotor system demonstrator
Avionics based on Xilinx Zynq 7020 MPSoC
HD Camera mounted on
3 Axis Gimbal
Motor Battery
Avionics Battery
Avionics developed and assembled by Students of the University of Oldenburg
in their master‘s project group

## Slide 4: Multi-rotor system‘s mixed-critical use-case
Source: www.robocup2010.org
Shoot robo soccer games with on-board camera
Use of a single chip avionics based on Zynq 7020
  Two main tasks:
  1. Flight algorithms (safety-critical)
  2. On-board video processing (non-/mission-critical)

## Slide 5: Task description
Safety-critical flight algorithms
  Sensor processing
  Remote control processing
  Attitude and altitude controller (standard PID)
  Failure  System will crash
Non-/Mission-critical object detection
  Video grabbing from camera
  Object detection
  Adjustment of camera gimbal to follow object
  Failure  Quality of Service
Safety-critical task has to be separated by the architecture to avoid all influences through other tasks

## Slide 6: State-of-the-art mixed-critical system design
Memory
CPU
HW IP
...
...
Memory
CPU
HW IP
F1
F2
F3
t
d2->3
F4
F5
t
d4->5
Application 1
Hard deadline d2->3
No power constraint
No temperature constraint
Application 2
Soft deadline d4->5
Hard power constraint
Hard temperature constraint
Fully distributed with dedicated HW/SW platforms for different criticalities
Extra-functional properties Timing, Power & Temperature
Safety-critical flight algorithms
Non-/Mission-critical object detection
F4
F5
F1
F2
F3

## Slide 7: Mixed-critical system design
Temporal, spatial, power and temperature segregation for mixed-critical control applications
Memory
CPU
HW IP
...
Memory
CPU
HW IP
...
Multi-core architecture
Memory
CPU 1
HW IP
...
CPU 2
running
block/susp.
shared var.
comm.
F1
F2
F3
t
d2->3
F1
F2
F3
F4
F5
t
d2->3
d4->5
<<virtual>>
<<virtual>>
<<virtual>>
<<virtual>>
<<virtual>>
<<virtual>>
F1
F2
F3
F4
F5
t
d4->5
F4
F5
Safety-critical flight algorithms
Non-/Mission-critical object detection

## Slide 8: Xilinx Zynq 7020 overview
Processing System
  Dual ARM Cortex A9
  866MHz
  Standard interfaces available
Programmable Logic
  Implementing own or IP hardware (further needed interfaces, processing elements, etc.)
  85.000 Logic Cells
Great for exploring architectures for mixed-criticality systems in consideration of extra-functional properties
  (Near future: Zynq UltraScale+)
Source: www.xilinx.com

## Slide 9: Avionics HW-architecture top-down
Motor Power Domain
Avionics Power Domain
Zynq industry board mounted on top of avionics
Distribution board allows
  Direct connection to sensors (accelerometers, gyroscopes, magnetometer, barometer)
  Direct connection to motor drivers
  Etc.
Separation in two power domains (motor & avionics)
  Since motors introduce much noise on the power lines
  Avoid failure of Zynq
Safety-Critical Part
Mission-Critical Part
PPM decoding IP core
ARM9 MP Cortex
A9 Core 0
Programming Logic
Camera
SD-Card
Motor Drivers
DPRAM 0
Battery Guards
Debug Pins
MPU9150
BMP085
RC Receiver
PPM IP
GPIO
GPIO
GPIO
GPIO
GPIO
GPIO
I2C IP
I2C IP
SPI IP
USB
Gimbal
Wi-Fi
SDIO
MicroBlaze 0
Data Mining
AMBA Interconnect
DPRAM 1
I2C IP
GPIO
MicroBlaze 1
Flight Control
A9 Core 1
GPIO
UART IP
DDR-RAM
DDR
L2 Cache
L1 Cache
L1 Cache
AXI Bus
AXI Bus
I/D RAM
I/D RAM
Debug Pins

## Slide 10: SW-Mapping
Safety-critical part
Non-/Mission-critical part
<<component>>
Data Mining
<<component>>
Video Processing
<<HW resource>>
ARM9 MP Cortex
<<processing resource>>
A9 Core 0
<<processing resource>>
A9 Core 1
<<OS>>
Linux kernel
<<alloc>>
<<alloc>>
<<alloc>>
<<HW resource>>
Programming Logic
<<processing resource>>
MicroBlaze 0
<<alloc>>
<<component>>
Flight Control
<<alloc>>
<<processing resource>>
MicroBlaze 1
Bare Metal
Bare Metal

## Slide 11: That‘s all…
Thank you! Any questions?
soeren.schreiner@offis.de